## Slide 1
A Hybrid Mixture-of-Experts
Architecture for Sensor-Attack
Detection in Water
Distribution Networks
Onur Ozan Sünger
MSc in Data Science
Supervisor: Prof. Francesca Cuomo
Co-supervisor: Tiziana Cattai
Academic year 2025–2026
Notes: Timing: 10 seconds (0:00–0:10).
Good morning. My thesis studies sensor-attack detection in water distribution networks. I will explain the architecture, how we tested it, and what the results show.
Sources and scope: Thesis title and abstract.

## Slide 2: Water distribution networks (WDNs)
Pipes connect water sources to consumers.
Pressure sensors monitor conditions in the network.
Modena
L-Town
272 nodes, 317 links
785 nodes, 909 links
268 junctions, 4 reservoirs
317 pipes
782 junctions, 2 reservoirs, 1 tank
905 pipes, 1 pump, 3 valves
Notes: Timing: 25 seconds (0:10–0:35).
A water distribution network carries water from sources to consumers through connected pipes. Pressure sensors monitor conditions in the network. We use two models: Modena, with 272 nodes and 317 links, and L-Town, with 785 nodes and 909 links. These diagrams show their actual layouts.
Sources and scope: Thesis Section 3.2 and network-component table. Counts independently checked against data/modena.inp and data/L-Town.inp. Layouts use their coordinates, vertices and connectivity, with independent coordinate scales. Node totals do not represent installed sensor counts.

## Slide 3: Problem statement
Detect five types of sensor-data attacks
in water distribution networks.
Modena: normal and attacked sensor examples
A
B
A Normal sensor
Reports an unaltered
pressure reading.
B Attacked sensor
Reports a pressure reading
modified by an attack.
Random, targeted, replay, drift and noise
Notes: Timing: 20 seconds (0:35–0:55).
Our task is to detect five types of sensor-data attacks. Here, sensor A reports an unaltered pressure reading, while an attack changes the reading from sensor B. We want reliable detection across all five attack families.
Sources and scope: Thesis Chapters 1 and 3. Modena layout from data/modena.inp. The two marked junctions represent illustrative sensor states, not an experimental observation or a real incident. The task concerns altered received pressure measurements across five attack families.

## Slide 4: Five attack mechanisms
We modify the pressure readings received by the detector.
Family | How the reading changes | Experimental setting
Random | Persistent bias at randomly selected sensors | Magnitude: 0.5–2.0 m
Targeted | Persistent bias at sensors selected by node degree | Magnitude: 0.5–2.0 m
Replay | An earlier observation replaces the current reading | Delay: 2–6 h
Drift | A bias increases gradually | Target: 0.5–2.0 m Ramp: 6–18 h
Noise | Random perturbations increase variability | Extra noise SD: 0.3–0.8 m
Pressure measurement noise: 0.1 m standard deviation (SD).
Notes: Timing: 45 seconds (0:55–1:40).
These are the five mechanisms and the settings used in our experiments. Random and targeted attacks add a persistent bias of half a metre to two metres. Their difference is how we select the sensors. Replay copies a reading from two to six hours earlier. Drift increases a bias gradually. Noise adds extra random variation. The normal measurement noise has a standard deviation of point one metres. These are controlled synthetic settings. Some attacks are more obvious than others, as the replay example will illustrate.
Sources and scope: Thesis Chapter 3 generator settings and attack equations; data/thesis_v2/ew_modena_modena_eval_seed40811/generate_config.yaml. Bias sign varies by episode. Drift target magnitude may not be reached before the episode ends. Extra noise SD is 3–8 times the 0.1 m measurement-noise SD, not the total SD. Controlled synthetic settings are not estimates from field attacks.

## Slide 5: The earlier cascade architecture
Sensor observations
Family router
Rank the experts
Candidate expert
Reconstruction and attack scores
Reconstruction + physics
Compare candidate consistency
Six graph-temporal experts
Normal + five attack families
Compare the next candidates.
Switch only for a clear
feedback improvement.
Retain the current choice or switch
Selected expert
Final sensor predictions
Notes: Timing: 35 seconds (1:40–2:15).
The earlier cascade had six graph-temporal experts: one for normal operation and one for each attack family. A router ranked the experts and selected a candidate. Reconstruction and physics consistency provided feedback, and the system could switch to another candidate. However, one selected expert still supplied the final prediction. This made the choice of expert central to detection performance.
Sources and scope: Existing cascade diagram preserved. Thesis Sections 4.2–4.4 describe the historical expert architecture and hard-selection diagnostics. Implementation detail: src/wdn/models/temporal_moe.py, expert_feedback_scores and cascade_route. The thesis hard-top-1 diagnostic evaluates selection without the complete feedback cascade.

## Slide 6: Why the architecture changed
Early cascade: attack-family F1
Modena development experiment, mean across 10 fitted runs
Chart: 
| Random | Targeted | Drift | Noise | Replay
Mean family F1 | 0.98725 | 0.99487 | 0.87968 | 0.85944 | 0.015079
Four families performed well. Replay F1 was only 0.015.
This motivated the search for reliable coverage across all five families.
Notes: Timing: 45 seconds (2:15–3:00).
In this early Modena experiment, random and targeted attacks achieved F1 scores close to point nine nine. Drift and noise were also above point eight five. Replay was the clear weakness, with F1 around point zero two. We wanted coverage across all five families, so this motivated a redesign. These are development results from a different setting, rather than a matched comparison with the final system. The thesis also examines weaknesses in hard expert selection and the reconstruction reference.
Sources and scope: Early-development context, separately supported by runs/temporal_moe/workshop_routing_v2.json: 10 fitted runs with data/v2_modena in run args. Mean cascade family F1: random 0.9873, replay 0.0151, drift (historical stealthy) 0.8797, noise 0.8594, targeted 0.9949. This archival diagnostic supplements the development account. It is not a matched comparison with the final hybrid. The evaluation follows the corrected scenario split and validation-calibrated thresholds in scripts/eval_workshop_routing.py. Thesis Sections 4.1 and 4.4–4.8 support the subsequent development narrative. The thesis Modena hard-top-1 versus soft-mixture diagnostic has its own population.

## Slide 7: Full hybrid workflow
INPUT DATA
1 Received pressure data
Normal reference
Estimated from other sensor groups
2 Model inputs: residual + temporal features
Input data describing pressure differences, trends and variability
3a General expert
Immediate at t
5 models + internal router
3b Drift expert
Gradual changes
Uses data up to t + 3 h
3c Noise expert
Unusual variability
Uses data up to t + 3 h
General alarm
passes directly
4 Checks on Drift / Noise alarm proposals
Routing + local feedback + verification
Accept supported additions, reject the rest
5 Final alarm = General OR accepted Drift OR accepted Noise
Otherwise: no alarm.
Notes: Timing: 75 seconds (3:00–4:15).
The final hybrid uses three parallel experts. First, we compare received pressure with a normal reference estimated from other sensor groups. The difference and its behaviour over time form the input features. All three experts receive this evidence. General combines five internal models and can raise an immediate alarm. Drift and Noise use temporal evidence, with access to data up to three hours later. A General alarm goes directly to the output. Additional Drift and Noise alarms pass routing, feedback and verification checks before acceptance. These checks can reject an additional alarm, but cannot cancel a General alarm. So the key design choices are a reference from other sensors, parallel expert evidence and checks on additional alarms. The output is an alarm decision; we do not implement an automatic countermeasure.
Sources and scope: Thesis Chapter 5, especially Sections 5.1–5.8. General's internal router forms a weighted mixture; the external router supplies mechanism context and veto evidence. The system still contains thresholds and gates. The redesign retains threshold decisions and routing, with a different role for each.

## Slide 8: How we tested the detector
1
Simulate normal operation
Generate pressure readings for Modena and L-Town.
2
Modify selected sensor readings
Apply five attack types and record which readings change.
3
Run the trained detector
Use separate evaluation scenarios and fixed thresholds.
4
Compare alarms with known labels
Count detections, missed attacks and false alarms.
Notes: Timing: 35 seconds (4:15–4:50).
We test the detector in four steps. First, we simulate normal pressure observations in Modena and L-Town. Second, we apply the five attack mechanisms and record exactly which readings change. Third, we run the trained detector on separate evaluation scenarios, with thresholds already fixed through calibration. Finally, we compare its alarms with the known labels and count detections, misses and false alarms. Let me show one example.
Sources and scope: Thesis Chapters 3 and 5. Separate training/calibration/evaluation scenarios; fixed calibration-selected thresholds. The subsequent replay example uses existing frozen evaluation outputs, without fitting or generating a new experiment.

## Slide 9: Replay detection in one sensor
Modena, sensor 18: a reading from 3 hours earlier
Normal reference
Unmodified reading
Replayed reading
Pressure (m)
Chart: 
| 129 | 130 | 132 | 133 | 134 | 137 | 138 | 139 | 142 | 143 | 144 | 145 | 146 | 147 | 149
Normal reference | 33.1232 | 33.9463 | 33.8734 | 34.1265 | 34.3309 | 32.4201 | 31.5203 | 32.2183 | 35.2501 | 35.8325 | 36.2034 | 36.4334 | 36.5416 | 36.6154 | 35.4338
Unmodified reading | 32.9756 | 33.9217 | 33.9873 | 34.2567 | 31.4432 | 32.213 | 35.8254 | 36.1861 | 36.6846 | 36.6926 | 35.4963
Replayed reading | 33.9217 | 34.2567 | 32.213 | 35.5485
General expert score
Decision threshold: 0.9852
Chart: 
| 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149
Threshold | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518 | 0.98518
Unmodified observation | 0.060104 | 0.019221 | 0.022772 | 0.016602 | 0.92157 | 0.92076 | 0.98282 | 0.96644 | 0.98307 | 0.95853 | 0.92516
Replayed observation | 0.045479 | 0.99864 | 0.99973 | 0.99935
Time (hours)
At hour 137
Received: 34.26 m
Expected: 32.42 m
The expert evaluates
this difference and
its recent history.
Score: 0.9986
Threshold: 0.9852
Alarm raised
Hybrid: 3 of 4 altered readings detected. 1 missed. 1 false alarm.
Notes: Timing: 75 seconds (4:50–6:05).
This is one replay example from the frozen Modena evaluation. Blue shows the normal reference, grey shows unmodified readings, and red shows the replayed readings. All four replayed values remain within the range of unmodified readings in this window. At hour 137, the reported pressure is 34.26 metres, while the reference is 32.42. The General expert evaluates the difference and temporal features. Its score is point 9986, above the fixed threshold of point 9852, so it raises an alarm. The lower plot shows the General scores. The complete hybrid detects three of the four altered readings and misses one. It also produces one additional false alarm through another expert. Missing readings have no points. This illustrates an actual decision, including its errors; it does not establish the difficulty of every attack.
Sources and scope: Frozen Modena evaluation: source 40811, fit 701, scenario 18 (zero-based), sensor name 18 / index 17. Episode hours 133–145 inclusive, lag 3 h. Modified observations at 133,137,142,145; General and hybrid detect the latter three. Hybrid false positive at 134, General does not alarm there. General threshold 0.985177646861955. Reference recovered as received minus frozen standardized residual times normal_error_scale (float32 precision). Lines connect available timestamps as guides; missing observations have no points. Data: data/thesis_v2/ew_modena_modena_eval_seed40811; frozen features: runs/operational/early_warning_multiseed_v1/features/modena_eval_seed40811/bank_seed40811.npz; scores: output/supervisor_revision_20261008/analysis/hybrid_scores/modena/seed701/evaluation_source40811.npz; decision rule: runs/operational/early_warning_multiseed_v1/stage_e_modena/seed/701/operating_points.json. This selected example illustrates detection and its errors, not overall attack difficulty or field validity.

## Slide 10: Final results on two networks
Final evaluation: 10 model fits × 6 sources per network
Mean metric | Modena | L-Town
Pooled F1 | 0.8669 | 0.8950
Family macro F1 | 0.9045 | 0.9083
Clean FPR (%) | 0.0584 | 0.0550
Modena: all five family means exceed 0.80.
L-Town: four exceed 0.89; replay remains at 0.7312.
168-hour scenarios; hourly readings; 50% pressure missingness.
24 scenarios per source. The 60 model–source cells are not independent.
Notes: Timing: 35 seconds (6:05–6:40).
The final results cover ten fitted models and six evaluation sources for each network. Pooled F1 is about point 867 in Modena and point 895 in L-Town. Family macro F1 is above point nine in both. Every family exceeds point eight in Modena. Replay remains the weakest family in L-Town, at point 7312. We report false alarms separately because detection performance alone does not describe the operational trade-off.
Sources and scope: Thesis Sections 6.2–6.4 and Table 6.1. Pooled F1 0.8669/0.8950; family macro F1 0.9045/0.9083; clean FPR percentages 0.0584/0.0550. Final L-Town replay 0.7312.

## Slide 11: Later refinements in each network
Modena: original confirmation with 5 model fits
Pooled F1 | Earlier hybrid | Threshold only | Integrated
5 fits × 6 sources | 0.6863 | 0.6998 | 0.8672
False positives fall by 84.2%, with 4.1% fewer true positives.
Drift and noise F1 fall slightly.
Extending to 10 fits gives the final mean of 0.8669.
L-Town: history comparison with 10 model fits
Mean metric | No history | History
Replay F1 | 0.7065 | 0.7312
Clean FPR (%) | 0.0627 | 0.0550
Replay improves in all 60 pairs, but still misses the 0.75 goal.
Notes: Timing: 30 seconds (6:40–7:10).
The later refinements address different weaknesses. In the matched Modena comparison, the integrated changes improved F1 and reduced false positives, with some loss of true positives. The point 8672 result uses five fitted models; point 8669 is the extended ten-model mean. In L-Town, history features improved replay from point 7065 to point 7312, although it remained below our point 75 research goal.
Sources and scope: Thesis Sections 6.5–6.6, Tables 6.2–6.3. Modena has 5 fits × 6 sources; the 10-fit extension in Section 6.5.2 gives 0.8669. L-Town has 10 fits × 6 shared sources. Each intervention uses its own paired baseline. Neither row is an old-cascade-versus-final-hybrid experiment.

## Slide 12: Overall scores against LightGBM
Same evaluation sources and three-hour information allowance
Network | Metric | LightGBM | Hybrid
Modena | Family macro F1 | 0.8593 | 0.9045
 | Pooled F1 | 0.8509 | 0.8669
 | Clean FPR (%) | 0.0317 | 0.0584
L-Town | Family macro F1 | 0.8823 | 0.9083
 | Pooled F1 | 0.8977 | 0.8950
 | Clean FPR (%) | 0.0184 | 0.0550
Original operating points. Bold marks the better score. Lower clean FPR is better.
Higher family macro F1 for the hybrid on both networks.
Fewer clean-period false alarms for the single LightGBM.
Pooled F1 favors the hybrid in Modena and slightly favors LightGBM in L-Town.
Notes: Timing: 35 seconds (7:10–7:45).
A strong single LightGBM model is an important control. Both systems use the same evaluation sources and a three-hour information allowance. The hybrid has higher family macro F1 in both networks. Its pooled F1 is higher in Modena, while LightGBM is slightly higher in L-Town. LightGBM also has a lower clean false-positive rate in both. The hybrid therefore does not win on every metric.
Sources and scope: Thesis Section 6.8, Tables 6.7–6.8. Single LightGBM is shown at its pooled-F1-selected operating point; hybrid uses its original frozen point. These are original operating-point comparisons on reused evaluation sources.

## Slide 13: Attack-family scores against LightGBM
Modena
Chart: 
| Random | Replay | Drift | Noise | Targeted
LightGBM | 0.974 | 0.906 | 0.7627 | 0.6742 | 0.9795
Hybrid | 0.9549 | 0.9283 | 0.8274 | 0.8439 | 0.968
L-Town
Chart: 
| Random | Replay | Drift | Noise | Targeted
LightGBM | 0.995 | 0.7084 | 0.8698 | 0.8422 | 0.9961
Hybrid | 0.992 | 0.7312 | 0.899 | 0.9279 | 0.9918
Hybrid leads on replay, drift and noise in both networks.
Mean family F1 at the reported operating points. LightGBM uses a 3-hour allowance.
Notes: Timing: 35 seconds (7:45–8:20).
The family scores explain the difference. At the reported operating points, the hybrid performs better on replay, drift and noise in both networks. LightGBM performs better on random and targeted attacks. So the hybrid improves coverage of the temporal attack families, while the single model remains competitive overall. This is why we report individual families alongside pooled F1.
Sources and scope: Thesis Tables 6.7–6.8. Family macro F1 is an equal-weight mean, not the minimum family score or a guarantee that every family improves.

## Slide 14: When is the hybrid useful?
Stronger coverage of temporal attacks
At the reported operating points, replay, drift and noise
F1 are higher on both networks than with single LightGBM.
A measurable cost in false alarms
LightGBM has lower clean FPR in both networks.
It also leads on random and targeted attacks.
The operating point matters
Calibration-derived threshold sweeps change the ranking.
The hybrid does not dominate across all operating points.
Notes: Timing: 25 seconds (8:20–8:45).
The hybrid is useful when stronger coverage of replay, drift and noise justifies additional complexity and false alarms. A simpler model may be preferable under a tighter false-alarm requirement. The operating point also matters: changing thresholds can change the ranking. We should assess that trade-off for the intended use.
Sources and scope: Thesis Sections 6.9–6.10, Appendix B and Chapter 7. General-only pooled F1 0.7200/0.8565 versus full 0.8669/0.8950. Verifier bypass clean FPR 0.4578%/0.3409% versus full 0.0584%/0.0550%. Sweeps are finite calibration-derived paths and not exhaustive frontiers.

## Slide 15: Conclusions
We built a detector for five sensor attack types.
Three experts analyse pressure data in parallel. General alarms
pass directly. Additional Drift and Noise alarms require checks.
We tested it on Modena and L-Town.
With simulated attacks and the reported thresholds, the hybrid
had higher replay, drift and noise F1 than LightGBM on both
networks. LightGBM raised fewer false alarms.
The next step is testing with operational data.
Measure incident detection, alert delays and runtime
before considering deployment.
Notes: Timing: 45 seconds (8:45–9:30).
We built a detector for five types of attacks on pressure readings. General, Drift and Noise analyse the data in parallel. General can raise an immediate alarm, while additional Drift and Noise alarms must pass checks. We tested this design on Modena and L-Town. Under the simulated attack conditions and reported thresholds, the hybrid achieved higher replay, drift and noise F1 than LightGBM in both networks. LightGBM raised fewer false alarms. The next step is to test operational data and measure incident detection, alert delays and runtime before considering deployment.
Sources and scope: Thesis Chapters 5–8, including the original-operating-point LightGBM comparisons. The comparison holds for the reported thresholds and simulated pressure-observation attack conditions; it does not assert uniform dominance or field validation. General retains its immediate alarm path; added Drift and Noise alarms require the prescribed checks. Incident-level evaluation, alert delays and computational measurements remain future work.

## Slide 16
Thank you for your attention.
Any questions?
Notes: Timing: 5 seconds (9:30–9:35).
Thank you for your attention. I am happy to take your questions.